## Slide 1: Computer Architecture Spring 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
BASIC COMPUTER ORGANIZATION AND DESIGN

## Slide 2: Outlines
Computer Architecture-Spring 2020, AUT, Tehran, Iran
• Instruction Codes
• Computer Registers
• Computer Instructions
• Timing and Control
• Instruction Cycle
• Memory Reference Instructions
• Input-Output and Interrupt
• Complete Computer Description
• Design of Basic Computer
• Design of Accumulator Logic

## Slide 3: INTRODUCTION
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Every different processor type has its own design (different registers, buses, microoperations, machine instructions, etc)
Modern processor is a very complex device
It contains
  Many registers
  Multiple arithmetic units, for both integer and floating point calculations
  The ability to pipeline several consecutive instructions to speed execution
  Etc.

## Slide 4: INTRODUCTION
Computer Architecture-Spring 2020, AUT, Tehran, Iran
However, to understand how processors work, we will start with a simplified processor model
This is similar to what real processors were like ~25 years ago
M. Morris Mano introduces a simple processor model he calls the Basic Computer
We will use this to introduce processor organization and the relationship of the RTL model to the higher level computer processor

## Slide 5: THE BASIC COMPUTER
Computer Architecture-Spring 2020, AUT, Tehran, Iran
The Basic Computer has two components, a processor and memory
The memory has 4096 words in it
  4096 = 212, so it takes 12 bits to select a word in memory
Each word is 16 bits long
CPU
RAM
0
4095
0
15

## Slide 6: INSTRUCTIONS
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Program
  A sequence of (machine) instructions
(Machine) Instruction
  A group of bits that tell the computer to perform a specific operation (a sequence of micro-operation)
The instructions of a program, along with any needed data are stored in memory
The CPU reads the next instruction from memory
It is placed in an Instruction Register (IR)
Control circuitry in control unit then translates the instruction into the sequence of microoperations necessary to implement it

## Slide 7: INSTRUCTION FORMAT
Computer Architecture-Spring 2020, AUT, Tehran, Iran
A computer instruction is often divided into two parts
  An opcode (Operation Code) that specifies the operation for that instruction
  An address that specifies the registers and/or locations in memory to use for that operation
In the Basic Computer, since the memory contains 4096 (= 212) words, we needs 12 bit to specify which memory address this instruction will use
In the Basic Computer, bit 15 of the instruction specifies the addressing mode (0: direct addressing, 1: indirect addressing)
Since the memory words, and hence the instructions, are 16 bits long, that leaves 3 bits for the instruction’s opcode
Opcode
Address
Instruction Format
15
14
12
0
I
11
Addressing
mode

## Slide 8: ADDRESSING MODES
Computer Architecture-Spring 2020, AUT, Tehran, Iran
The address field of an instruction can represent either
  Direct address: the address in memory of the data to use (the address of the operand), or
  Indirect address: the address in memory of the address in memory of the data to use
Effective Address (EA)
  The address that can be directly used without modification to access an operand for a computation-type instruction, or as the target address for a branch-type instruction
0
ADD
457
22
Operand
457
1
ADD
300
35
1350
300
Operand
1350
+
AC
+
AC
Direct addressing
Indirect addressing

## Slide 9: PROCESSOR REGISTERS
Computer Architecture-Spring 2020, AUT, Tehran, Iran
A processor has many registers to hold instructions, addresses, data, etc
The processor has a register, the Program Counter (PC) that holds the memory address of the next instruction to get
  Since the memory in the Basic Computer only has 4096 locations, the PC only needs 12 bits
PC
12-bit

## Slide 10: PROCESSOR REGISTERS
Computer Architecture-Spring 2020, AUT, Tehran, Iran
In a direct or indirect addressing, the processor needs to keep track of what locations in memory it is addressing
  The Address Register (AR) is used for this
  The AR is a 12-bit register in the Basic Computer
When an operand is found, using either direct or indirect addressing, it is placed in the Data Register (DR)
  The processor then uses this value as data for its operation
The Basic Computer has a single general purpose register – the Accumulator (AC)

## Slide 11: PROCESSOR REGISTERS
Computer Architecture-Spring 2020, AUT, Tehran, Iran
The significance of a general purpose register is that it can be referred to in instructions
  e.g. load AC with the contents of a specific memory location; store the contents of AC into a specified memory location
Often a processor will need a scratch register to store intermediate results or other temporary data
  In the Basic Computer this is the Temporary Register (TR)

## Slide 12: PROCESSOR REGISTERS
Computer Architecture-Spring 2020, AUT, Tehran, Iran
The Basic Computer uses a very simple model of input/output (I/O) operations
  Input devices are considered to send 8 bits of character data to the processor
  The processor can send 8 bits of character data to output devices
The Input Register (INPR) holds an 8 bit character gotten from an input device
The Output Register (OUTR) holds an 8 bit character to be send to an output device

## Slide 13: BASIC COMPUTER REGISTERS
Computer Architecture-Spring 2020, AUT, Tehran, Iran
List of BC Registers
  DR 16 Data Register Holds memory operand
  AR 12 Address Register Holds address for memory
  AC 16 Accumulator Processor register
  IR 16 Instruction Register Holds instruction code
  PC 12 Program Counter Holds address of instruction
  TR 16 Temporary Register Holds temporary data
  INPR 8 Input Register Holds input character
  OUTR 8 Output Register Holds output character
11
0
PC
15
0
IR
15
0
TR
7
0
OUTR
15
0
DR
15
0
AC
11
0
AR
INPR
0
7
Memory
4096 x 16
CPU

## Slide 14: COMMON BUS SYSTEM
Computer Architecture-Spring 2020, AUT, Tehran, Iran
The registers in the Basic Computer are connected using a bus
This gives a savings in circuitry over complete connections between registers

## Slide 15: COMMON BUS SYSTEM
Computer Architecture-Spring 2020, AUT, Tehran, Iran

## Slide 16: COMMON BUS SYSTEM
Computer Architecture-Spring 2020, AUT, Tehran, Iran
AR
PC
DR
L
I
C
L
I
C
L
I
C
AC
L
I
C
ALU
E
IR
L
TR
L
I
C
OUTR
LD
INPR
Memory
4096 x 16
Address
Read
Write
16-bit Common Bus
7
1
2
3
4
5
6
S0
S1
S2

## Slide 17: COMMON BUS SYSTEM
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Three control lines, S2, S1, and S0 control which register the bus selects as its input
Either one of the registers will have its load signal activated, or the memory will have its read signal activated
  Will determine where the data from the bus gets loaded
The 12-bit registers, AR and PC, have 0’s loaded onto the bus in the high order 4 bit positions
When the 8-bit register OUTR is loaded from the bus, the data comes from the low order 8 bits on the bus
0 0 0 x
0 0 1 AR
0 1 0 PC
0 1 1 DR
1 0 0 AC
1 0 1 IR
1 1 0 TR
1 1 1 Memory
S2 S1 S0 Register

## Slide 18: to be continued
Computer Architecture-Spring 2020, AUT, Tehran, Iran