## Slide 1: Computer Architecture Spring 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
BASIC COMPUTER ORGANIZATION AND DESIGN

## Slide 2: Outlines
Computer Architecture-Spring 2020, AUT, Tehran, Iran
• Instruction Codes
• Computer Registers
• Computer Instructions
• Timing and Control
• Instruction Cycle
• Memory Reference Instructions
• Input-Output and Interrupt
• Complete Computer Description
• Design of Basic Computer
• Design of Accumulator Logic

## Slide 3: BASIC COMPUTER INSTRUCTIONS
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Basic Computer Instruction Format
15 14
12 11
0
I
Opcode
Address
Memory-Reference Instructions (OP-code = 000 ~ 110)
Register-Reference Instructions (OP-code = 111, I = 0)
Input-Output Instructions (OP-code =111, I = 1)
15
12 11
0
Register operation
0 1 1 1
15
12 11
0
I/O operation
1 1 1 1

## Slide 4: BASIC COMPUTER INSTRUCTIONS
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Hex Code
Symbol I = 0 I = 1 Description
  AND 0xxx 8xxx AND memory word to AC
  ADD 1xxx 9xxx Add memory word to AC
  LDA 2xxx Axxx Load AC from memory
  STA 3xxx Bxxx Store content of AC into memory
  BUN 4xxx Cxxx Branch unconditionally
  BSA 5xxx Dxxx Branch and save return address
  ISZ 6xxx Exxx Increment and skip if zero
  CLA 7800 Clear AC
  CLE 7400 Clear E
  CMA 7200 Complement AC
  CME 7100 Complement E
  CIR 7080 Circulate right AC and E
  CIL 7040 Circulate left AC and E
  INC 7020 Increment AC
  SPA 7010 Skip next instr. if AC is positive
  SNA 7008 Skip next instr. if AC is negative
  SZA 7004 Skip next instr. if AC is zero
  SZE 7002 Skip next instr. if E is zero
  HLT 7001 Halt computer
  INP F800 Input character to AC
  OUT F400 Output character from AC
  SKI F200 Skip on input flag
  SKO F100 Skip on output flag
  ION F080 Interrupt on
  IOF F040 Interrupt off

## Slide 5: INSTRUCTION SET COMPLETENESS
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Instruction Types
A computer should have a set of instructions so that the user can
construct machine language programs to evaluate any function that is known to be computable.
  Functional Instructions
  - Arithmetic, logic, and shift instructions
  - ADD, CMA, INC, CIR, CIL, AND, CLA
  Transfer Instructions
  - Data transfers between the main memory
  and the processor registers
  - LDA, STA
  Control Instructions
  - Program sequencing and control
  - BUN, BSA, ISZ
  Input/Output Instructions
  - Input and output
  - INP, OUT

## Slide 6: to be continued
Computer Architecture-Spring 2020, AUT, Tehran, Iran