## Slide 1: Computer Architecture Spring 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology

## Slide 2: Copyright Notice
Computer Architecture, Spring 2020, AUT, Tehran, Iran
Lectures adopted from
Computer Organization and Design: The Hardware/Software Interface, 5th edition, David A. Patterson, John L. Hennessy, MK pub., 2014
  Chapter 5: Large and Fast: Exploiting Memory Hierarchy

## Slide 3: Replacement Policy
Computer Architecture, Spring 2020, AUT, Tehran, Iran
Direct mapped: no choice
Set associative
  Prefer non-valid entry, if there is one
  Otherwise, choose among entries in the set
Cache replacement policies (algorithms)

## Slide 4: Replacement Policy
Computer Architecture, Spring 2020, AUT, Tehran, Iran
Cache replacement policies (algorithms)
  Bélády's optimal algorithm (or simply optimal)
  FIFO
  LIFO (or FILO)
  Most-recently used (MRU)
  Random
  Least-recently used (LRU)
Bélády's anomaly
  The phenomenon in which increasing the number of blocks results in an increase in the number of misses for certain memory access patterns
Fine more: https://en.wikipedia.org/wiki/Cache_replacement_policies

## Slide 5: LRU Replacement Policy
Computer Architecture, Spring 2020, AUT, Tehran, Iran
Age bits: show the accesses order
  Number of bits per block: Log n for n-way cache